## Slide 1
PNMF / EVIDENCE REVIEW
Evaluating PNMF's
Physical-Model Validity
Current evidence, improvement priorities, and explicit limits.
Advisor review | 03 August 2026
Validity boundary
Physically coherent.
Software-auditable.
Conceptual screening only.
Not certification evidence.
Notes: [Sources]
Scope and wording: projects/pnmf/docs/ADVISOR_PRESENTATION_TEXT.md; projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
No external assets used.

## Slide 2
01 / CURRENT VERDICT
Validity is claim-specific, not binary
PNMF | physical-model validity | 2
The current route clears a software and physical-coherence bar. It does not yet clear an independent measurement-validity bar.
Claim
Current evidence
Status
What remains unproven
Physical plausibility
Mechanistic scaling + SI boundary
SUPPORTED
Measurement residuals
Implementation correctness
Unit, gate, provenance, regression tests
SUPPORTED
Real-world accuracy
A320-211 anchoring
Frozen fit to ANP SEL/LAmax
CONDITIONAL
Independent component proof
Predictive / transfer validity
No component ledger or held-out family study
NOT DEMONSTRATED
Unseen engine/configuration behavior
Use the status language to keep physical claims proportional to evidence.
Notes: [Sources]
Implementation evidence: projects/pnmf/pnmf/physics.py; projects/pnmf/tests/test_physics.py.
Calibration and route boundary: projects/pnmf/pnmf/api.py; projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Evidence framing: NASA Dahl, https://ntrs.nasa.gov/citations/20080032565.

## Slide 3
02 / AUDIT METHOD
A validity claim needs four pieces of evidence
PNMF | physical-model validity | 3
Every technical statement in the deck follows the same audit pattern.
CLAIM
What do we want
to say?
EVIDENCE
What does the
checkout show?
LIMITATION
Where does the
claim stop?
NEXT PROOF
What data would
upgrade it?
A passing unit test is evidence for implementation behavior, not a substitute for a measured component comparison.
Notes: [Sources]
Audit structure: projects/pnmf/docs/PHYSICAL_MODEL_IMPROVEMENT_RESEARCH.md.
Validation practice: ECAC Doc 29, 5th Edition, Volume 1, https://www.ecac-ceac.org/images/documents/ECAC-CEAC-DOC_29_5th_Edition-REPORT_ON_STANDARD_METHOD_OF_COMPUTING_NOISE_CONTOURS_AROUND_CIVIL_AIRPORTS-Volume_1-APPLICATIONS_GUIDE.pdf.
No external assets used.

## Slide 4
03 / PROPULSION PHYSICS
Simplified source laws show the key inputs
PNMF | physical-model validity | 4
JET / Stone-style mixing
Iⱼₑₜ ∝ ρⱼ² · Aⱼ · Vⱼ⁸
Lⱼₑₜ ≈ Cⱼₑₜ + 80 log₁₀(Vⱼ/c₀) + 10 log₁₀(Aⱼ)
fₚₑₐₖ ≈ 0.25 · fₛ꜀ₐₗₑ · Vⱼ / Dⱼ
Velocity dominates; detailed streams add density/pressure state. Fallback stays visible.
FAN / Heidmann-style path
L𝒇𝒂𝒏 ≈ C𝒇𝒂𝒏 + 10 log₁₀(ṁ) + 40 log₁₀(Mₜᵢₚ)
BPF = Uₜᵢₚ · Nᵦₗₐdₑₛ / (π · D)
Uₜᵢₚ = Mₜᵢₚ · c₀
Detailed fan paths add temperature-rise, spacing, tone, and lobe terms; fallback stays visible.
Evidence dependency: mass flow, nozzle state, fan diameter, RPM/blade count, temperature rise, and provenance.
Notes: [Sources]
Equations: projects/pnmf/pnmf/physics.py, module documentation and StoneSource/FanSource implementations.
Input contract: projects/pnmf/pnmf/physics.py (EnginePhysicalInputs, FanDeck, JetStream).
Improvement rationale: projects/pnmf/docs/PHYSICAL_MODEL_IMPROVEMENT_RESEARCH.md; NASA jet assessment https://ntrs.nasa.gov/citations/20080032565.

## Slide 5
04 / PROPAGATION AND METRICS
A short event calculation keeps the boundary visible
PNMF | physical-model validity | 5
AIRFRAME / Fink-style laws
L𝒘ᵢₙ𝓰/𝒇ₗₐₚ ∝ 50 log₁₀(V/c₀)
L𝓰ₑₐᵣ ∝ 60 log₁₀(V/c₀)
δ* = 0.37 · c̄ · Re⁻⁰·²
Area, flap angle, wheel count, diameter, and directivity refine each component; six outputs remain inspectable.
PROPAGATION / EVENT OUTPUT
Lₚ(f,r) = L₁ₘ(f) − 20 log₁₀(r / 1 m) − α(f)·r
Lₜₒₜₐₗ = 10 log₁₀(Σᵢ 10^(Lᵢ/10))
SEL = 10 log₁₀[(1/1 s) ∫ 10^(Lᴬ(t)/10) dt]
Lᴬ,ₘₐₓ = maxₜ Lᴬ(t)
A-weighting is applied before the two metrics; the reference event is 160 kt, straight-level, 69 angles.
160 kt straight-level reference event | 69 emission angles | SEL + LAmax only
Notes: [Sources]
Airframe, propagation, and metric equations: projects/pnmf/pnmf/physics.py; projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Reference event: projects/pnmf/pnmf/physics.py (Reference160KtFlightPath, NPD_REF_SPEED_MS).
Metric boundary: projects/pnmf/pnmf/api.py (physics route supports SEL and LAmax only).

## Slide 6
05 / WORKED EXAMPLE
One reference event shows how measurements become a bounded prediction
PNMF | physical-model validity | 6
A320-211 | BPR 6.0 | 160 kt reference event | SEL + LAmax
1 MEASURE / SPECIFY
ANP truth curve
aircraft + BPR
input status
→
2 CALCULATE SOURCES
jet + fan
wing/slat + flap
gear spectra
→
3 PROPAGATE
spreading
absorption
A-weighting
→
4 PREDICT
energetic sum
SEL + LAmax
NPD row
Observed residuals: calibration RMSE 1.57 dB | out-of-sample mean 3.01 dB | maximum 4.85 dB
Observed residual RMSE by aircraft (dB)
Chart: dB
| A320-211 | 727EM2 | A350-941 | 747200 | 757PW | 767300 | A320-232 | MD82 | 777300 | 737300 | A330-343 | 737800 | 757RR
RMSE | 1.57 | 4.85 | 4.64 | 3.55 | 3.27 | 2.89 | 2.82 | 2.82 | 2.56 | 2.42 | 2.29 | 2.25 | 1.77
Signed bias: prediction − truth (dB)
Chart: dB
| A320-211 | 727EM2 | A350-941 | 747200 | 757PW | 767300 | A320-232 | MD82 | 777300 | 737300 | A330-343 | 737800 | 757RR
Bias | -0.13 | 3.79 | 3.63 | -2.2 | 2.11 | -1.41 | 2 | 2.34 | 0.8 | -1.19 | 0.87 | -0.82 | 1.1
Observed residual summaries from physics_fleet_validation.csv; RMSE/bias are not confidence intervals or certification margins.
Notes: [Sources]
Worked calculation chain: projects/pnmf/pnmf/physics.py (EngineState, JetSource, FanSource, AirframeSource, propagation, SEL/LAmax); projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Reference event and calibration: projects/pnmf/pnmf/physics.py (Reference160KtFlightPath, PhysicsNPDModel.calibrate); projects/pnmf/pnmf/api.py.
Residual charts: projects/pnmf/outputs/physics_fleet_validation.csv, generated by projects/pnmf/pnmf_cli.py (frozen constants, prediction minus ANP truth, A320-211 calibration plus 12 out-of-sample aircraft).
Interpretation: RMSE and bias are observed residual summaries, not confidence intervals; projects/pnmf/pnmf/validation.py.

## Slide 7
06 / ONE-AIRCRAFT CALCULATION
A320-211: one complete calculation from inputs to noise level
PNMF | physical-model validity | 7
Departure example | 22,500 lb/engine | 1,000 ft observer | 160 kt reference event
CASE + DERIVED STATE
Aircraft A320-211 / CFM56-5A1
BPR 6.0
Engines 2
Fmax 25,000 lb/engine
P 22,500 lb/engine
V 82.31 m/s
d 304.8 m
Angles 69 (5° to 175°)
v_j 282.08 m/s
ṁ 354.81 kg/s
A_j 1.604 m²
d_j 1.429 m
M_tip 1.140
BPF 1,859 Hz
Engine-deck streams unavailable; fallback source paths and estimated geometry are visible.
FORMULATION / LaTeX SOURCE
F = P_{eng}(4.44822),
v_j = \frac{700}{(1+BPR)^{0.44}}\sqrt{\frac{F}{F_{max}}},
\dot m = \frac{F}{v_j},\quad A_j = \frac{\dot m}{\rho_j v_j},
d_j = \sqrt{\frac{4A_j}{\pi}},\quad
f_{peak} = f_{scale}\,0.25\frac{v_j}{d_j}
L_{i}(f,r_k) = L_{i,1m}(f) - 20\log_{10}(r_k/1m) - \alpha(f)r_k
r_k = \frac{d}{\sin\theta_k},\quad t_k = \frac{-d\cot\theta_k}{V}
L_A(t_k) = 10\log_{10}\sum_i 10^{L_{A,k}^{(i)}/10}
L_{A,max} = \max_k L_A(t_k),\quad
SEL = 10\log_{10}\left[\frac{1}{1s}\int 10^{L_A(t)/10}dt\right]
Source spectra are A-weighted after propagation, then summed energetically. SEL integrates the 69-point receiver history; LAmax takes its peak.
RESULT VS DATA
Metric
ANP
ET
Physics
SEL
96.40
96.40
97.27
LAmax
88.90
88.90
87.27
Physics − ANP
SEL +0.87 dB
LAmax −1.63 dB
Physics component SEL
jet 94.40 dB
fan 94.05 dB
airframe 76.03 dB
total 97.27 dB
Error = prediction − ANP truth. ANP is the real-aircraft benchmark; ET is in-sample for this A320-211 row, not held-out evidence.
Notes: [Sources]
Numerical case: projects/pnmf/pnmf_cli.py (A320-211 / BPR 6.0 fleet context); projects/pnmf/pnmf/physics.py (PhysicsDesign, EngineState, Reference160KtFlightPath, EventDiagnostics).
Formulation: projects/pnmf/docs/NPD_SYSTEM_DESIGN.md, section 3.3; projects/pnmf/pnmf/physics.py (JetSource, FanSource, AirframeSource, propagation, SEL/LAmax).
ANP benchmark: CFM565 A320-211 rows in the local ANP truth database (SEL/LAmax, departure, 22,500 lb, 1,000 ft).
ET comparison: projects/pnmf/pnmf/api.py (NoisePredictor) and projects/pnmf/pnmf/models.py.
The displayed values are a traceable reference calculation, not a measurement-validity or certification claim.

## Slide 8
07 / FORMULA REFERENCE
LaTeX formulation: source spectra become receiver metrics
PNMF | physical-model validity | 8
Copy these blocks into PowerPoint's equation editor and keep the comparison definition unchanged.
1 / SOURCE LEVEL
2 / PROPAGATE + SUM
3 / COMPARE TO DATA
I_{jet}\propto\rho_j^2 A_j v_j^8
L_{jet,1m}=C_j+80\log_{10}(v_j/c_0)
\quad+10\log_{10}(A_j)+D_j(\theta)+H_j(f)
L_{fan,1m}=C_f+10\log_{10}(\dot m)
\quad+40\log_{10}(M_{tip})+D_f(\theta)+H_f(f)
L_{air,1m}=C_a+p\log_{10}(V/c_0)
\quad+G_a+D_a(\theta)+H_a(f),\quad p\in\{50,60\}
r_k=\frac{d}{\sin\theta_k},\quad
t_k=\frac{-d\cot\theta_k}{V}
L_i(f,r_k)=L_{i,1m}(f)
-20\log_{10}(r_k/1m)-\alpha(f)r_k
L_{A,k}^{(i)}=10\log_{10}\sum_f
10^{[L_i(f,r_k)+A(f)]/10}
L_A(t_k)=10\log_{10}\sum_i
10^{L_{A,k}^{(i)}/10}
L_{A,max}=\max_k L_A(t_k)
SEL=10\log_{10}\left[\frac{1}{1s}
\int 10^{L_A(t)/10}dt\right]
e_{phys}=y_{phys}-y_{ANP}
e_{ET}=y_{ET}-y_{ANP}
RMSE=\sqrt{\frac{1}{n}\sum e_i^2}
\quad bias=\frac{1}{n}\sum e_i
A320-211 at 1,000 ft: ANP = 96.40 / 88.90 dB, ET = 96.40 / 88.90 dB, physics = 97.27 / 87.27 dB (SEL / LAmax).
Notes: [Sources]
Source laws and symbols: projects/pnmf/docs/NPD_SYSTEM_DESIGN.md, section 3.3; projects/pnmf/pnmf/physics.py (JetSource, FanSource, AirframeSource).
Propagation and metrics: projects/pnmf/pnmf/physics.py (propagate, EventDiagnostics, SEL/LAmax).
Comparison definitions: projects/pnmf/pnmf/validation.py (prediction minus truth, RMSE, bias); projects/pnmf/pnmf/api.py (independent ET and physics routes).
The LaTeX is provided as editable source text for manual PowerPoint equation conversion.

## Slide 9
08 / SOFTWARE EVIDENCE
Tests verify behavior; they do not validate reality
PNMF | physical-model validity | 9
The existing suite is valuable evidence, but each test has a bounded claim.
Test family
What it supports
What it does not prove
Status
Units and scaling
A-weighting, absorption, jet Vⱼ⁸, gear V⁶, BPR sensitivity
Correctness of the chosen physical law for a new engine
SUPPORTED
Source gates
Detailed jet/fan/core paths and six airframe outputs appear only when inputs permit
That the available inputs describe the real aircraft
SUPPORTED
Calibration behavior
Four anchors and spectral factor affect the documented reference fit
Independent component accuracy or transferability
CONDITIONAL
Metric and provenance
SEL/LAmax scope, unavailable states, and separate truth/prediction tables
A measured uncertainty interval or certification claim
SUPPORTED
Software verification closes implementation questions; measurement validation closes physical-accuracy questions.
Notes: [Sources]
Tests: projects/pnmf/tests/test_physics.py.
Implementation: projects/pnmf/pnmf/physics.py; projects/pnmf/pnmf/api.py.
Validation distinction: NASA Dahl, https://ntrs.nasa.gov/citations/20080032565; ECAC Doc 29, 5th Edition, Volume 1, official applications guide.

## Slide 10
09 / COMPONENT VALIDITY
Component mechanisms remain the weakest evidence layer
PNMF | physical-model validity | 10
Implemented mechanisms are inspectable; independent component measurement evidence is the missing link.
Component
Implemented basis
Missing evidence
Status
Jet
Stone-style mixing; Vⱼ⁸ scaling; multi-stream gate
Measured spectra/directivity by state
CONDITIONAL
Fan
Heidmann scaling; BPF; inlet/discharge lobes
Engine-deck and flight component data
CONDITIONAL
Core
Optional branch; unavailable without complete core state
Any component evidence in current workflow
NOT DEMONSTRATED
Wing / slat
Fink-style 50 log₁₀(V/c₀) + geometry proxies
Modern high-lift component measurements
CONDITIONAL
Flap edges
Main and side-edge spectra separated
Interaction and configuration evidence
CONDITIONAL
Main gear
Fink-style 60 log₁₀(V/c₀) + wheel/diameter terms
Gear and flap-wake interaction data
CONDITIONAL
Nose gear
Separate wheel/strut source
Component-resolved measurements
CONDITIONAL
System sum
Energetic combination + propagation + metrics
Held-out event and aircraft-family tests
NOT DEMONSTRATED
Evidence upgrade order: component spectra/directivity -> propagated event -> total SEL/LAmax -> NPD transfer.
Notes: [Sources]
Component implementation: projects/pnmf/pnmf/physics.py; projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Input/preset limitations: projects/pnmf/docs/PHYSICS_PRESETS.md.
Evidence ladder: projects/pnmf/docs/PHYSICAL_MODEL_IMPROVEMENT_RESEARCH.md; NASA airframe measurements https://ntrs.nasa.gov/citations/20220006685; NASA fan flight effects https://ntrs.nasa.gov/citations/20220006704.

## Slide 11
10 / CALIBRATION BOUNDARY
Calibration anchors the system, not the components
PNMF | physical-model validity | 11
CALIBRATION EVIDENCE
A320-211
BPR 6.0
ANP SEL + LAmax
Four additive anchors + one spectral-placement factor are fitted, then frozen.
VALIDATION STILL NEEDED
| independent component spectra and directivity
| held-out event states and aircraft families
| measurement plus model-form uncertainty
| transfer limits tied to real input provenance
A fit can make the reference curve agree while leaving component mechanisms or new configurations untested.
Notes: [Sources]
Calibration code and contract: projects/pnmf/pnmf/physics.py (PhysicsNPDModel.calibrate); projects/pnmf/pnmf/api.py.
Reference data context: projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Calibration-versus-validation method: NASA Dahl, https://ntrs.nasa.gov/citations/20080032565; NASA uncertainty assessment https://ntrs.nasa.gov/citations/20190000984.

## Slide 12
11 / TRANSFER LIMITS
Applicability shrinks when state or mechanism is missing
PNMF | physical-model validity | 12
The output remains useful only inside a documented state envelope.
Input / path
Current practice
Validity consequence
Report as
Engine deck
Detailed state is optional; named fallback remains
Fallback may dominate the source spectrum
ESTIMATED
Geometry
Preset span/BPR plus estimated high-lift and strut fields
Mechanism fidelity varies by aircraft
ESTIMATED
Trajectory
160 kt straight-level reference event
No segmented or operational-profile claim
CONDITIONAL
Propagation
Free-field spreading + molecular absorption
Installation, shielding, ground, terrain and lateral effects excluded
EXCLUDED
Metric
SEL and LAmax
EPNL/PNLTM tone corrections are outside physics route
BOUNDED
Explicit exclusions: installation/shielding, nacelle treatment, ground reflection, lateral attenuation, terrain, and non-uniform atmosphere.
Notes: [Sources]
Applicability and exclusions: projects/pnmf/pnmf/physics.py (EventDiagnostics.excluded_effects); projects/pnmf/docs/NPD_SYSTEM_DESIGN.md; projects/pnmf/docs/PHYSICS_PRESETS.md.
Metric scope: projects/pnmf/pnmf/api.py.
Method rationale: ECAC Doc 29, 5th Edition, Volume 1 official applications guide.

## Slide 13
12 / IMPROVEMENT CAMPAIGN
Validation should proceed from components to systems
PNMF | physical-model validity | 13
Do not jump directly from one calibrated reference curve to a universal accuracy claim.
1 COMPONENT
Spectra + directivity
Jet, fan, airframe
measured by state
2 SYSTEM EVENT
Held-out SEL/LAmax
Propagated history
and total metric
3 TRANSFER
Aircraft/configuration
New family, state,
or installation bound
Validation record | dataset/version/hash | aircraft/engine state | geometry/configuration | observer | corrections + uncertainty | residual | calibration/holdout tag
The ledger makes evidence portable, reviewable, and separable from training data.
Notes: [Sources]
Validation campaign design: projects/pnmf/docs/PHYSICAL_MODEL_IMPROVEMENT_RESEARCH.md.
Data separation and provenance: projects/pnmf/docs/ADVISOR_PRESENTATION_TEXT.md; projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Primary methodology: NASA Dahl https://ntrs.nasa.gov/citations/20080032565; NASA airframe component measurements https://ntrs.nasa.gov/citations/20220006685.

## Slide 14
13 / ACCEPTANCE BAR
Stronger claims require explicit evidence gates
PNMF | physical-model validity | 14
The gate is about evidence quality and reproducibility, not a target accuracy number.
01
Predeclare metrics, tolerances, and comparison protocol
02
Compare component spectra/directivity against measurements
03
Validate held-out system-event SEL/LAmax
04
Separate measurement, input, and model-form uncertainty
05
Load a versioned calibration artifact without silent refit
06
Tie applicability labels to actual evidence coverage
07
Keep excluded physics and unquantified uncertainty visible
Claim upgrade
NOT DEMONSTRATED
+ component evidence
CONDITIONAL
+ held-out transfer
SUPPORTED FOR A BOUND
No invented intervals. No universal claim outside the evidence range.
Notes: [Sources]
Acceptance logic: projects/pnmf/docs/PHYSICAL_MODEL_IMPROVEMENT_RESEARCH.md.
Auditability, reliability, consistency, accuracy, and input-quality principles: ECAC Doc 29, 5th Edition, Volume 1, https://www.ecac-ceac.org/images/documents/ECAC-CEAC-DOC_29_5th_Edition-REPORT_ON_STANDARD_METHOD_OF_COMPUTING_NOISE_CONTOURS_AROUND_CIVIL_AIRPORTS-Volume_1-APPLICATIONS_GUIDE.pdf.
Uncertainty wording: projects/pnmf/pnmf/physics.py (uncertainty_note).

## Slide 15
14 / CONCLUSION
Current verdict: bounded validity, not predictive proof
PNMF | physical-model validity | 15
PNMF's physical route is ready for disciplined conceptual screening.
Its strongest claims today are physical coherence, software auditability, and explicit scope. Its weakest claims are component accuracy, cross-aircraft transfer, and quantitative uncertainty.
SUPPORTED NOW
coherence | provenance
implementation checks | bounded metrics
EARNED NEXT
component evidence | held-out events
transfer bounds | calibrated uncertainty
Future physics work starts after the evidence gate, not before it.
Notes: [Sources]
Current scope and boundary: projects/pnmf/docs/ADVISOR_PRESENTATION_TEXT.md; projects/pnmf/docs/NPD_SYSTEM_DESIGN.md.
Future priorities: projects/pnmf/docs/PHYSICAL_MODEL_IMPROVEMENT_RESEARCH.md.
No numerical accuracy or certification claim is made.